Swift 2.5 HS

These are the setup we used on the test model ; it is just for a starting point.

CG : 8 cm from wing leading edge,

STD flight : aileron and flap at 0; elevator +/- 8mm (at the outmost of moving part);

aileron + 11mm -7mm (at the outmost part);

rudder +/-35 degree

Speed : no need of a special setup for speed

Start : as above, but flap down 5mm

Butterfly : flap all down , aileron up 15 mm , differential off, elevator down 1,5mm (at outmost part)